## Slide 1: Data Collection/Process Monitoring
Notes: Practice good process management

## Slide 2: Recordkeeping
Good recordkeeping is essential
Records allow site managers to measure performance against goals, comply with rules, make better compost, and plan.
“Operating Record” refers to all the data that provides details and documentation of the facility’s status and operating history.

## Slide 3: Common Records
Production
  Tons in/tons out
  In-process
Process
  Temperature
  Turns
  Moisture
Regulatory
  Pathogen Reduction
  Heavy Metals
  Inerts
Finished Product
  Micronutrients
  Stability/maturity
  pH
  Electrical conductivity
  Organic matter

## Slide 4: Temperature
Notes: The single most useful measurement that things are working.

## Slide 5: Testing for Moisture
Drying oven
Weighing the dried sample
Wet Weight - Dry Weight / Wet Weight x 100 = Moisture percentage

## Slide 6: Quick Test for Moisture
Digital scale
Notice the operators are outside
Microwave oven
Wet Weight - Dry Weight / Wet Weight x 100 = Moisture percentage
Notes: Example: Wet Weight = 100 grams
Dry Weight = 60 grams
100 grams – 60 grams/ 100 grams x 100 = 40%
- The units don’t matter, as long as they are consistent
- Use 100 (units) or 10 (units) to keep the math easy
- Don’t forget to subtract the weight of the container (Tare)

## Slide 7
Just right!
(50 to 60% water by weight)
Moisture – Squeeze Test
Notes: Some feedstocks (especially manures) can hold even more moisture.

## Slide 8: O2/CO2 Monitoring

## Slide 9: Measuring Bulk Density

## Slide 10: pH?
Affordable hand-held meters available
More commonly done by a lab.
TMECC Methods exist

## Slide 11: Questions?

## Slide 12: An Introduction to Lab Testing
Notes: Because you can’t tell that much from looking at it!

## Slide 13: First, Take a good sample

## Slide 14: No, Really, you Need to Take a Good Sample
https://www.compostfoundation.org/Sampling-Video
Notes: Random & Representative
Take a good sample, handle and store it pr
Get it to the lab expeditiouslyoperly

## Slide 15: Laboratory Testing
You need a relationship with a lab.
Regular testing is critical
Use compost (not soil or water) methods
TMECC
May be required for regulatory compliance
May be required for sales & marketing

## Slide 16
Compliance First:
Metals
Pathogens
Physical
Contaminants
R
R
R

## Slide 17
Stability: Degree of Completion
Maturity: Plant Beneficial

## Slide 18
Physical and Chemical
Characteristics

## Slide 19
Physical and Chemical
Characteristics
Organics Matter/Ash
C:N Ratio
Moisture
Conductivity/eC5

## Slide 20
Physical and Chemical
Characteristics
Nutrients, etc.

## Slide 21: Lab Testing Wisdom
Understand when the lab needs the sample and what volumes and sample times are (send on a Tuesday, not a Friday).
Make sure you are using a compost lab (not a water or soil lab) or at least compost methods (TMECC).
If you fail a regulatory test. Do not panic. Re-examine your sampling and handling procedures and re-send a new sample.
Do additional tests based on what customers want to see.
Don’t be afraid to ask the lab questions: great resource.

## Slide 22: Questions?